## Slide 1
Antenna
AD9226
Analog to digital converter
64MHz sampling rate
PC running Vivado (AMD) to program the Zynq FPGA via JTAG
EBAZ2405 Board
Zynq7010 FPGA
Ethernet 100 Mb/s
Local user
view/zoom spectrogram/waterfall
TODO:
listen SSB ham radio
decoding digital modes (FT8) by WSJT-X
A/D Samples
12 bits
WSJT-X
Full 0 – 32 MHz Spectrum and Waterfall

## Slide 3
AD9226 output

## Slide 4
Block diagram
A/D
DDC
Audio
65MSps
0 – 1v
256 KSps
DMA
DDC
Waterfall

## Slide 5
Shielded ADC
Shielded power supply filter (TODO)
USB <-> JTAG
&
USB <-> UART
16 wires ADC <-> FPGA (PL)
EBAZ4205 board with Zynq-7000 (PS+PL)
UART
JTAG
Ethernet

## Slide 7
PC I7 10750
16 GB RAM – 2 TB SSD
Windows 10 or 11
12V 500mA
Test points
Ethernet
100 Mbits/sec
Ethernet
100 Mbits/sec
100/1000 Mbits/sec
(option: Internet)
USB
VIVADO 2021.2 for Windows
ORACLE VM VirtualBox 6.1.38
UBUNTU 20.04.1
PetaLinux Tools 2021.2
USB to
UART + JTAG
UART
JTAG
32GB SD

## Slide 8
Start
Y
N
In Vivado:
Create a basic block design
Generate bitstream (.bit)
Export hardware (.xsa)
In PetaLinux:
Create a project
Configure it with the «Exported Hardware» (.xsa)
Build
Package (.wic)
In BalenaEtcher:
Flash the .wic package to a MicroSD (32GB)
On EBAZ4205:
Boot from MicroSD
Check if Ethernet is working
In Vivado:
Modify the block design
Generate bitstream (.bit)
Convert .bit to .bin with bootgen
Send .bin to EBAZ4205 via JTAG
On EBAZ4205:
Check if the new block design is working as expected
In Vitis:
Create/Modify an app
Debug it on EBAZ4205
Y
N
1) Set an initial basic block design on Vivado, prepare a Linux SD Card and first boot EBAZ4205
2) Modify the block design on Vivado and test the results on EBAZ4205
3) Modify/Debug the Standalone/Linux App on Vitis IDE and test the results on EBAZ4205
Check if the App is working as expected
3 macro steps to design / test the Programmable Logic and the Linux / Standalone software
End

## Slide 9
WinSCP:
Browse the Linux folders
Copy From/To Windows To/From Linux
Vitis IDE:
Debug / Run Linux Apps on EBAZ4205 via TCF (TCP port 1534)
Debug / Run Standalone Apps on EBAZ4205 via JTAG
Oscilloscope:
Examine hardware signals on testpoints
SSH (via IP) or TTY (via UART) EBAZ4205 Console:
Run Linux Apps
Configure Linux (Ethernet, Web Server, ALSA, …)

## Slide 10
Sampler
Audio DDC
Data
Capture
16384 x 32 bits
I2S
ADC
12 bits + OverRange
13 bits (12 bits + OTR) – 64 MSps
Clocking Wizard
64MHz
64 MSps
X
X
CIC - I
4-8192
FIR – I
2
Memory mapped I/O
TCP Server
Ethernet
Zynq 7010 Programmable Logic
Zynq7010 PS (CPU)
DDS
100K – 32 MHz
Ethernet
Windows 10 PC
EXTIO
EBAZ4205 DLL
HPSDR
CIC - Q
4-8192
FIR – Q
2
DEMOD
AM
LSB / USB
+
AGC
PCM 5102
(Digital to Analog)
Amplifier
16 (12)
2x16(16)
16(16)
16(16)
32 (13)
32(29)
I2S 32(29)
Switch
Test Generator
0.1-30 MHz
AM modulated 1KHz
16 (12)

## Slide 11
Sampler
Audio DDC
Data
Capture
16384 x 32 bits
I2S
ADC
12 bits + OverRange
13 bits (12 bits + OTR) – 64 MSps
Clocking Wizard
64MHz
64 MSps
X
X
CIC - I
4-8192
FIR – I
2
Memory mapped I/O
Ethernet
Zynq 7010 Programmable Logic
Zynq7010 PS (CPU)
DDS
100K – 32 MHz
CIC - Q
4-8192
FIR – Q
2
DEMOD
AM
LSB / USB
+
AGC
PCM 5102
(Digital to Analog)
Amplifier
16 (12)
2x16(16)
16(16)
16(16)
32 (13)
32(29)
I2S 32(29)
Switch
Test Generator
0.1-30 MHz
AM modulated 1KHz
16 (12)
I2S
I2S
PS/2
mouse
HDMI TX
Simple Framebuffer
Mouse driver
zgpio dev/input/event0
sdr-app
QT5 - C++
/dev/uio0
…
/dev/uio8

## Slide 12
Sampler
Audio DDC
Data
Capture
16384 x 16 bits
ADC
12 bits + OverRange
13 bits (12 bits + OTR) – 64 MSps
Clocking Wizard
64MHz
64 MSps
Memory mapped I/O
Ethernet
Zynq 7010 Programmable Logic
Zynq7010 PS (CPU)
DDS
10K – 32 MHz
CIC - Q
4-8192
FIR – Q
2
AM DEMOD
PCM 5102
(Digital to Analog)
Amplifier
16 (12)
16 (13)
32(29)
I2S 32(29)
Test Generator
0.1-30 MHz
AM modulated 1KHz
16 (12)
I2S
PS/2
mouse
HDMI TX
Simple Framebuffer
Mouse driver
zgpio dev/input/event0
sdr-app
QT5 - C++
/dev/uio0
…
/dev/uio8
Spectrum
DDC
DDS
2K – 32 MHz
CIC - IQ
4-8192
FIR–IQ
2
Data
Capture
2 x 16384 x 16 bits
X
X
Ampl
X1-1024
Switch
Configurable from / readable from /
write to /
PS (CPU)

## Slide 13
Sampler
Data
Capture
16384 x 32 bits
ADC
12 bits + OverRange
13 bits
64 MSps
64MHz
clock
13 bits
64 MSps
Memory mapped I/O
TCP Server
Ethernet
Zynq 7010
Programmable Logic
Zynq7010 PS (CPU)
Ethernet
Windows 10 PC
SpectrumPy
RF test generator
100KHz-30MHz
MUX
(switch)
Set Frequency

## Slide 14
Sampler
Data
Capture
16384 x 32 bits
ADC
12 bits + OverRange
13 bits
64 MSps
64MHz
clock
13 bits
64 MSps
Memory mapped I/O
TCP Server
Ethernet
Zynq 7010
Programmable Logic
Zynq7010 PS (CPU)
Ethernet
Windows 10 PC
SpectrumPy
RF test generator
100KHz-30MHz
MUX
(switch)
Set Frequency

## Slide 15
AD9226 board
Original schematic of the analog input
With SENSE = GND, the full scale between VINA and VINB is 2 Vpp
i.e.
VINA – VINB = +1V D11…D0=0xFFFFFF
VINA – VINB = 0V D11…D0=0x7FFFFF
VINA – VINB = -1V D11…D0=0x000000
The overall amplification between VINA-VINB and INPUT_50_Ohm is approximatively:
200//62
-------------------- x (200/200 + 1) = 0,38 i.e. -8,4 dB
200 + 200//62

## Slide 16
0 32 64 96 128 MHz

## Slide 17
Two’s complement:
R35: not connected
R34: 10 KOhm
Straight Binary :
R35: 10 KOhm
R34: not connected
ADC9226 board
Change data outputs from Straight Binary to Two’s Complement

## Slide 18
CIC filter
R=4…8192 decimation
N=6 stages
FIR filter
L=110 coefficients
Fs=64MHz Fs/R Fs/R .
R | Bandwidth = Fs/R * 0.25 (Hz) | Fs/R (Hz) | Example
4 | 2M | 16M | Spectrum
8 | 1M | 8M | Spectrum
16 | 0.5M | 4M | Spectrum
32 | 0.25M | 2M | Spectrum
64 | 0.125M | 1M | Spectrum
128 | 62K | 0.5M | Spectrum
256 | 30K | 0.25M | AM / Spectrum
512 | 15K | 0.125M | AM
1024 | 8K | 62K | DSB / AM
2048 | 4K | 30K | FT8 / USB / LSB
4096 | 2K | 15K | FT8 / CW
8192 | 1K | 8K | WSPR / CW
Bandwith can range from 1KHz to 2MHz changing decimation rate (R) only
CIC compensation by FIR is indipendent from R (for R>=4)
CIC compensation
High (>120dB) stopband attenuation
Filter Model

## Slide 19
LSB
USB
AM
AM SSB Demodulator and AGC
X
X
SIN
COS
I
Q
+
-
MUX
X
X
+
SQRT
Audio
Local Oscillator (BFO) 10KHz
HIGH PASS
AGC
Automatic Gain Control
Weaver SSB Demodulator
AM Demodulator
to I2S
16(15)
16(15)
32(30)
32(31)
16(16)
16(16)
16(16)
32(31)
32(32)
>> 16
16(16)
>> 16
16(16)
32(32)
16(16)
16(16)
xx(yy) is a xx bits two’s complement number with maximum value representable with yy bits e.g.
32 (28) is a 32 bits binary number, with
-(2^27) <= value <= (2^27) -1
LOW PASS
Level Meter

## Slide 20
Automatic Gain Control
2) then it is attenuated by 256 (2^8) so that the input signal can be attenuated / amplified
2^-8 2^8
1) The input signal is amplified with a gain between 1 and 65535 (unsigned 16 bit)
3) Every 1/48000 seconds (sampling rate), Gain is:
increased by Attack - e.g. 8 if output is lower than 2^30
decreased by Decay (e.g. -16) ifoutput is higher than 2^30
Input = 2^30*sin(2*pi*3000) + 2^30*sin(2*pi*400) i.e.
-2^31 <= input <= 2^31 -1
To test the AGC, an input signal (in yellow) of amplitude 2^32 is alternated with the same signal of amplitude 2^32/200 (-46dB) every 2 seconds
The decay time
For 50 msecs set Decay = -16
The attack time
For 100 msecs set Attack = 8
The output is in blue
Before the attenuation could take place in Decay time, the output signal is clipped (distorted) by the two’s complement 32 bit overflow
(+ - 2.147.483.648)